The Assembly Language of the Boz–5

The Boz–5 uses bits 31 – 27 of the IR as a five–bit opcode.

Of the possible 32 opcodes, only 26 are implemented.

| Op-Code | Mnemonic | Description |
| --- | --- | --- |
| 00000 | HLT | Halt the Computer |
| 00001 | LDI | Load Register from Immediate Operand |
| 00010 | ANDI | Logical AND Register with Immediate Operand |
| 00011 | ADDI | Add Signed Immediate Operand to Register |
| 00100 | NOP | Not Yet Defined – At Present it is does nothing |
| 00101 | NOP | Not Yet Defined – At Present it is does nothing |
| 00110 | NOP | Not Yet Defined – At Present it is does nothing |
| 00111 | NOP | Not Yet Defined – At Present it is does nothing |

This strange gap in the opcodes caused by not using 4, 5, 6, and 7 is an example of adjusting the ISA to facilitate a simpler design of the control unit.

With this grouping, the instructions with a “00” prefix either have no argument or have an immediate argument; in short, no memory reference.

More Opcodes

Here are the opcodes in the range 8 to 15.

| Op-Code | Mnemonic | Description |
| --- | --- | --- |
| 01000 | GET | Input from I/O Device Register to Register |
| 01001 | PUT | Output from Register to I/O Device Register |
| 01010 | RET | Return from Subroutine |
| 01011 | RTI | Return from Interrupt (Not Implemented) |
| 01100 | LDR | Load Register from Memory |
| 01101 | STR | Store Register into Memory |
| 01110 | JSR | Call a subroutine. |
| 01111 | BR | Branch on Condition Code to Address |

Here we begin to see some structure in the ISA.

The “01” prefix is shared by all instructions that generate memory address references.  This grouping simplifies the design of the Major State Register, which is an integral part of the control unit.

The Last Opcodes

| Op-Code | Mnemonic | Description |
| --- | --- | --- |
| 10000 | LLS | Logical Left Shift |
| 10001 | LCS | Circular Left Shift |
| 10010 | RLS | Logical Right Shift |
| 10011 | RAS | Arithmetic Right Shift |
| 10100 | NOT | Logical NOT (One’s Complement) |
| 10101 | ADD | Addition |
| 10110 | SUB | Subtraction |
| 10111 | AND | Logical AND |
| 11000 | OR | Logical OR |
| 11001 | XOR | Logical Exclusive OR |

The instructions with the “10” and “11” prefix, in short all with the single–bit prefix of “1”, are register–to–register operations, with no memory reference.

Again, one sees this grouping in an attempt to simplify the control unit.

Syntax of the Assembly Language

Immediate Operations

The syntax of the immediate operations is quite simple.

Syntax	Example

LDI %RD, value	LDI %R3, 100
	ANDI %RD, %RS, value	ANDI %R5, %R3 0xFFA08
	ADDI %RD, %RS, value	ADDI %R5, %R2, 200
	NOP	NOP

Most implementations of immediate addressing have only one register in the machine language instruction.  Our implementation with two registers is again due to considerations of simplifying the control unit.

In the AND Immediate instruction, the immediate operand is zero extended to 32 bits before being applied.  Let R3 contains the 32–bit number 0x77777777.

| R3 | 0111 | 0111 | 0111 | 0111 | 0111 | 0111 | 0111 | 0111 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FFA08 | 0000 | 0000 | 0000 | 1111 | 1111 | 1010 | 0000 | 1000 |
| Result | 0000 | 0000 | 0000 | 0111 | 0111 | 0010 | 0000 | 0000 |

Syntax of the Assembly Language (Part 2)

Input / Output Operations

Syntax	Example

GET %Rn, I/O_Reg	GET %R2, XX	
		// Load the general-purpose register from
		// the I/O device register.
	PUT %Rn, I/O_Reg	PUT %R0, YY	
		// Store the contents of register into the 
		// I/O device register.

Load/Store Operations

The syntax of these is fairly simple.  For direct addressing we have the following.

Syntax	Example
	LDR %Rn, address	LDR %R3, X	Loads %R3 from address X
	STR %Rn, address	STR %R0, Z		Loads %R0 into address Z
						This clears M[Z]

Syntax of the Assembly Language (Part 3)

Branch

The syntax of this instruction, and its variants, is quite simple.

Syntax							Example

BR Condition_Code, address		BRU 5, W

The condition code field determines under which conditions the Branch instruction is executed.  The eight possible options are.

Condition Code
		Decimal	Binary	Action
		0	000	Branch Always	(Unconditional Jump)
		1	001	Branch on negative result
		2	010	Branch on zero result
		3	011	Branch if result not positive
		4	100	Branch if carry–out is 0
		5	101	Branch if result not negative
		6	110	Branch if result is not zero
		7	111	Branch on positive result

Syntax of the Assembly Language (Part 4)

Unary Register-To-Register

| 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Op Code |  | Destination Register | Source Register | 5–bit Shift Count (0 – 31) | Not Used |

Opcode = 	10000	LLS	Logical Left Shift

10001	LCS	Circular Left Shift

10010	RLS	Logical Right Shift

10011	RAS	Arithmetic Right Shift

10100	NOT	Logical NOT (Shift count ignored)

NOTES:	1.	If (Count Field) = 0, a shift operation becomes a register move.
	2.	If (Source Register = 0), the operation becomes a clear.
	3.	Circular right shifts are not supported, because they may be 
		implemented using circular left shifts.
	4.	The shift count, being a 5 bit number, has values 0 to 31 inclusive.

Shift Examples

Here are figures showing the varieties of right shifts on signed 8–bit integers.

Syntax of the Assembly Language (Part 5)

Binary Register-To-Register

| 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Op Code |  | Destination Register | Source Register 1 | Source Register 2 | Not used |

Opcode =	10101	ADD	Addition

10110	SUB	Subtraction

10111	AND	Logical AND

11000	OR	Logical OR

11001	XOR	Logical Exclusive OR

NOTES: Subtract with (Destination Register) = 0 becomes a compare to set condition codes.

Syntactic Sugar

Syntactic Sugar	Assembled As	Comments

CLR %R2	LDI %R2, 0	Clears the register
CLW X	STR %R0, X	Clears the word at address X
INC %R2	ADDI %R2,  1	Increments the register
DEC %R2	ADDI %R2, -1	Decrements the register

NOP	LLS %R0, %R0, 0	No-Operation: Does Nothing RCS %R3, %R1, 3	LCS %R3, %R1, 29

Right circular shift by N is the same as left circular by (32 – N).  The shift count must be a constant number.

DBL %R2	LLS %R2, %R2, 1	Left shift by one is the
			same as a multiply by 2.

MOV %R2, %R3	LSH %R2, %R3, 0	Shift by 0 is a copy.

NEG %R4, %R5	SUB %R4, %R0, %R5	Subtract from %R0 ( 0 
			is the same as negation.

Syntactic Sugar (Part 2)

Syntactic Sugar	Assembled As	Comments

TST %R1	SUB %R0, %R1, %R0

This compares %R1 to zero by subtracting %R0 from it, discarding the result.

CMP %R1, %R2	SUB %R0, %R1, %R2

Determines the sign of(%R1) – (%R2), discarding the result.

BRU	BR 000	Branch always

BLT	BR 001	Branch if negative
BEQ	BR 010	Branch if zero

BLE	BR 011	Branch if not positive
BCO	BR 100	Branch if carry out is 0
BGE	BR 101	Branch if not negative
BNE	BR 110	Branch if not zero
BGT	BR 111	Branch if positive